## Slide 1
DMR Repeater Tune and Test
DR600
TR850

## Slide 2
Test Equipment
1
PC software Installation
2
Tune Parameter
3
Parameter Test
4
Content

## Slide 3
Test Cable
1、Test connecting cable
2、RF connecting cable
3、False battery
Test Equipment
1、DC/AC Power supply
2、HP8921A
3、IFR3920
4、pc
5、Multimeter
Test Equipment
1
Analog Analyzer HP8921A
Manufacturer: HP
Digital Analyzer IFR3920 with DMR option
Manufacturer: Aeroflex

## Slide 4
1、Install pc software
Please open the pc installation and install it according to instruction
2. Set test password
1) Add a new txt file in the installation directory and name it to “adjustmode”. Then run the programming software again.
2) The tune mode will be shown under the menu of program. Note: It is only allow to enter to turn mode when repeater connected to PC well.
PC Software Installation
2

## Slide 5
Program test frequency
Tune Parameter
3
 | TR850-01\DR600-01【136~174MHz】 |  | TR850-02\DR600-02【400~470MHz】 | 
Ch | TX(MHz) | RX(MHz) | TX(MHz) | RX(MHz)
Ch1 | 136.0250 | 136.2250 | 400.0250 | 400.2250
Ch2 | 144.0250 | 144.2250 | 418.0250 | 418.2250
Ch3 | 154.9875 | 154.9875 | 434.9875 | 434.9875
Ch4 | 155.0250 | 155.2250 | 435.0250 | 435.0250
Ch5 | 163.0250 | 163.2250 | 453.0250 | 453.0250
Ch6 | 174.9875 | 174.9875 | 469.9875 | 469.9875

## Slide 6
Tune Low and High power
Tune Parameter
4
Set the HP8921 to tx mode.
Enter to pc tune mode
Double click “high pow” to adjust high power . Please adjust each frequency.
After adjust, please click “OK” to save it.
Refer to the above steps to tune low power.
High Power | VHF | 45.0W±2W
 | UHF | 40W±2W
Low Power | 20W±0.2W | 
Suggested Power value for high and low :
Move it to adjust power value
Click PTT to enter tx

## Slide 7
Frequency Stability
Tune Parameter
3
Set the mode to “TX mode” on the HP8921
Enter to PC tune mode
Double click “Low Freq.Mod Deviation”
Adjust the value on PC until the TX freq error is within “±40Hz” on the HP8921
Then Click “OK” to save it.
Please use the same method to adjust high frequency .Mod Deviation
Frequency Stability | ±40Hz

## Slide 8
Low frequency modulation deviation
High frequency modulation deviation
Parameter Tune
3
Set HP8921 to tx test mode
Enter to PC tune mode
3.Double Click “LF modulation deviation” and click F1 to F6 to adjust the pc data to adjust the deviation to 5.0±0.05kHz
4.Click ok to save it
Low Frequency modulation deviation | 5.0±0.05kHz
High Frequency modulation deviation | 5.0±0.05kHz
Filter 1:50Hz HPF
Filter 2: 15KHz LPF

## Slide 9
RF RX sensitivity
Parameter Tune
3
Set the HP8921 to RX TEST mode
Enter to pc tune mode
3.Double click “RF rx sensitity” and enter to F1 to F6 to adjust its sensitivity
4.Set amplitude to -119dBm, and set the RF frequency to F1 to F6 ,then adjust pc data to keep the SINAD to maximum and above 12dB
RX sensitivity | SINAD>=12dB
Amplitude:-119dBm
Filter 1:300Hz HPF
Filter 2: 3KHz LPF
Set to 16
RF Gen Freq: rx frequency of radio
Set to 3KHz

## Slide 10
SQL1 Open and Close
Parameter Tune
3
Set the HP8921 to RX test mode
Enter to PC tune mode
3.Double Click “SQL1 Open” and enter to F1 to F6 in sequence, then click “Start”. When the data on pc is stable, click stop.
4.Then click “:OK “ to save it.
SQL | Open | -123dBm
 | Close | -125dBm
Adjust this value according to SQL open and close lever
Wide band:3kHz
Narrow band:1.5kHz
RF Gen Freq:RX frequency of radio

## Slide 11
SQL9 Open, SQL9 Close
Parameter Tune
3
Set the HP to RX test
Enter to pc tune mode
Double click “SQL9 Open” and enter to F1 to F6 in sequence.
4. Click “Start”, when the data is stable, click “stop’.
5. After adjust all the freuqnecy, click “ok” to save the data
6. Use the same way to adjust the SQL9 Close.
SQL9 | Open | -116dBm
 | Close | -119dBm
Adjust this value according to SQL open and close lever
Wide band:3kHz
Narrow band:1.5kHz
RF Gen Freq:RX frequency of radio

## Slide 12
Test frequency stability
Test the parameter
4
Tune Mode: Manual
Set the HP8921 to tx test.
Press ptt to transmit
View the TX Freq Error
Frequency stability | ±100Hz
Set the tx frequency of your radio

## Slide 13
Test High/Low Power
Test the parameter
4
Set the HP8921 to Tx test
Press PTT to transmit
View the tx power value on HP8921,and view the current value on DC power supply.
Use the same way to test the low , mid and high frequency.
Tune Mode : Auto
Input Port: RF In
High Power | VHF | 5.0W±0.1W
 | UHF | 4.2W±0.1W
Low | 1.0W±0.2W | 
Current(H) | <1.8A
Current(L) | <1A

## Slide 14
Test the max deviation
Test the parameter
4
Tune Mode : Auto
AFGenl Freq:1KHz
Set HP8921 to tx test
Press PTT to transmit
View the FM deviation on the HP8921.
Use the same way to test the Low, mid and high frequency.
25KHz | 3.8kHz~4.8KHz;
12.5KHz | 1.8kHz~2.5kHz。
Modulation Sensitivity:50mV
Filter 1:50Hz HPF
Filter 2: 15KHz LPF

## Slide 15
Test the wide band modulation sensitivity
Test the parameter
4
AFGenl Freq:1KHz
Set HP8921 to tx test mode.
Switch the channel to wide band. (25k), then press PTT to transmit.
Adjust the value of AF Gen Lv1 to let the FM deviation equal to 3k. The value of AF Gen1 LV1 is the modulation sensitivity
Modulation Sensitivity | 12mV±5mV
Filter 1:300Hz HPF
Filter 2: 3KHz LPF

## Slide 16
Narrow band modulation sensitivity
Test the parameter
4
AFGenl Freq:1KHz
Set the HP to Tx test
Switch the channel to Narrow band(12.5K),then press PTT to transmit
Adjust the value of AF Gen1 Lv1 and let the FM Deviation to 1.5K. The value of “AF Gen1 Lv1”is the modulation sensitivity.
Filter 1:300Hz HPF
Filter 2: 3KHz LPF
Modulation Sensitivity | 12mV±5mV

## Slide 17
Test Tx distortion
Test the parameter
4
AFGenl Freq:1KHz
Set the HP8921 to TX mode
Set the filter from 300Hz to 3Khz. Set the AFGen1 Freq to 1K.
Press the PTT to transmit. Adjust the value of Gen1 Lv1 to let the FM Deviation to 3K.
Now set the Distn ,refer to picture. Please check the value of Distn. The distorting should be less than 3%.
5. Use the same way to test all the Low, high and middle frequency.
Tx Distortion | ＜3%
Modulation
Sensitivity
Filter 1:300Hz HPF
Filter 2: 3KHz LPF

## Slide 18
Tx S/N
Test the parameter
4
AFGenl Freq:1KHz
Set the HP8921 to TX mode. Filter :300Hz-3KHz.
AF Gen1 Freq:1KHz
AF Gen1 Lv1: modulation sensitivity.
Set the mode: SNR
2. Press PTT to transmit and view the value of SNR.
3. Use the same way to test Low, middle and high frequency.
SNR(Wide) | ＞45dB
SNR(Narrow) | ＞35dB。
Modulation Sensitivity
Filter 1:300Hz HPF
Filter 2: 3KHz LPF

## Slide 19
Test the deviation of QT、DQT
Test the parameter
4
HP8921: TX mode
Filter:<20Hz HPF, 300Hz LPF。
2. Press PTT to transmit
3. And view the value of FM deviation.
Filter 1: <20Hz HPF
Filter 2:300Hz LPF
Deviation (Wide) | 0.5~0.9kHz
Deviation (Narrow) | 0.25~0.5kHz

## Slide 20
Test VOX-1
Test the parameter
4
HP8921:TX
AF Gen1 Lv1”:50mV。
2. Switch to the VOX channel. The radio will transmit automatically.
3. When turn of the signal of AF Gen1 Lv1, the radio will stop transmit.
VOX 1 | 50mV

## Slide 21
Test the max audio output
Test the parameter
4
HP8921： Rx Test.
Rotate the volume to maximum.
View the AC Level on HP8921 and view the current on power supply.
Use the same way to test wide band and narrow band.
Filter 1:300Hz HPF
Filter 2: 3KHz LPF
Set to 16
Wide band:3kHz
Narrow band:1.5kHz
Amplitude:-47dBm
Max Audio output | 1.4W ±0.2W
Current | ＜0.5A
RF Gen Freq: RX frequency of radio

## Slide 22
Test Rx Sensitivity
Test the parameter
4
HP8921: Rx Test.
Rotate the volume and adjust volume to half of maximum value.(0.5W)
View the value of SINAD.
Use the same way to test low, middle, high frequency.
Filter 1:300Hz HPF
Filter 2: 3KHz LPF
Wide band:3kHz
Narrow band:1.5kHz
RX Sensitivity | SINAD>=12dB
Amplitude:-119dBm
RF Gen Freq: rx frequency of the radio

## Slide 23
Test SQL1
Test the parameter
4
Wide band:3kHz
Narrow band: 1.5kHz
Set HP8921 to RX Test.
Set the SQL level to 1
Adjust the value of Amplitude. View the RX status of radio. It can open and close its SQL at the designed input. Please refer to the following form.
Use the same way to test low, middle and high frequency.
RF Gen Freq: Rx Frequency of radio
SQL1 Open | >-119dBm
SQL1 Close | <-127dBm
Filter 1:300Hz HPF
Filter 2: 3KHz LPF

## Slide 24
SQL9
Test the parameter
4
Wide band:3kHz
Narrow band:1.5kHz
HP8921： Rx Test.
Set the radio SQL level to 9
Adjust the value of Amplitude
View the RX status of radio.
It can receive when the input signal is above -116dBm
It will stop receive when the input signal is below -119dBm.
RF Gen Freq:rx frequency of radio
SQL9 Open | >-116dBm
SQL9 Close | <-119dBm
Filter 1:300Hz HPF
Filter 2: 3KHz LPF

## Slide 25
Test RSSI
Test the parameter
4
HP8921： Rx Test.
Set the value of Amplitude to-107dBm,. View the RSSI Icon on the radio, it should have one bar. Set the value of Amplitude to -70dBm. Wiew the RSSI Icon on the radio, it should have four bars.
RF Gen Freq: Rx frequency of radio
Wide band:3kHz
Narrow band: 1.5kHz
Input -107dBm | One bar
Input -70dBm | Four bars

## Slide 26
RX Distortion
Test the parameter
4
HP8921： Rx Test
Adjust the volume knob and adjust the volume to half of Maximum.(0.5w)
Set HP8921 to Distn. （Refer to the picture）
View the Distn value on the HP8921. It should be less than3%
Use the same way to test other frequencies
Filter 1:300Hz HPF
Filter 2: 3KHz LPF
Tx Distortion | ＜3%
Wide band:3kHz
Narrow band:1.5kHz
Amplitude: -47dBm
RF Gen Freq: RX frequency of the radio

## Slide 27
RX S/N
Test the parameter
4
Filter 1:300Hz HPF
Filter 2: 3KHz LPF
HP8921： Rx Test
Adjust the volume knob and adjust the volume to half of Maximum.(0.5w)
Set HP8921 to SNR. （Refer to the picture）
View the SNR value on the HP8921. Refer to normal parameter in following form.
Use the same way to test other frequencies.
SN(Wide) | ＞45dB
SN(Narrow) | ＞35dB。
Wide band:3kHz
Narrow band: 1.5kHz
Amplitude:-80dBm
RF Gen Freq:RX Frequency of radio

## Slide 28
Test the decode of CTCSS
Test the parameter
4
HP8921:RX
Switch the channel to CTC/DSC channel
Open AF Gen2 and set its frequency to the matched frequency of the radio ctc. Set the value of AFGen2 to 0.5 for Wide band and 0.35 for narrow band. The radio will unmute.
Turn off the AFGen2, the radio will mute.
Use the same way to test other frequency.
Wide band:3kHz
Narrow band: 1.5kHz
Wide band: 0.5kHz
Narrow band:0.35kHz
Amplitude:-120dBm
RF Gen Freq: Your radio RX frequency
设置为CTCSS频率

## Slide 29
CDCSS decode
Test the parameter
4
Wide band:3kHz
Narrow band 1.5kHz
HP8921： Rx Test.
Enter to encode interface.
3.Select send , the radio will unmute. When select stop the radio will mute.
RF Gen Freq :your radio rx frequency
Set the mode to CDCSS
Set to cont
CDCSS\
Enter to encode mdoe
Set to
Wide band 0.75kHz
Narrow band: 0.35kHz

## Slide 30
TX 4FSK error、TX EVM error、TX BER
Test the parameter
4
In the tune mode, you can find the 4FSK error, please enter to it
Set the 3920 to DMR test mode.
Set the receiver frequency to your radio TX frequency.
Press PTT to transmit, and view the FSK error and EVM on the 3920.
Use the same way to test other frequency.
TX 4FSK Error | ≤5%
EVM Error | ≤1%
TX BER | 0%

## Slide 31
RX BER
Test the parameter
4
Enter to test mode in programming software
Set the 3920 to DMR test mode，Set theTransmit to the frequency of your radio tx. Out the standard signal(0.153,std 511)
Adjust the value of LV1，and view the BER on the radio. Stop to adjust this value until the the BER is 5%. Record the LV1 on the 3920.
Use the same way to test other frequency.
≤-120dBm时 | BER<5%

## Slide 32
Tks!