Product Interface Definition

( DMR Product )

| Revision version | Date | Author | Description | Remarks |
| --- | --- | --- | --- | --- |
| V1.0 | 2022-9-26 | Lucas | None | None |

Content

Content	1

1 DP980/DP990/DP680 Accessory Interface	2

1.1 Interface Diagram	2

1.2 Interface Definition and Function Introduction	2

1.3 PCB Interface Layout	4

2 DM850/TM840/DM880 Transceiver Accessory Interface	4

2.1 Front Panel Microphone Interface	4

2.1.1 Interface Diagram	4

2.2 Interface Definition and Function Introduction	5

2.2.1 PCB Interface Layout	6

2.3 Tail Pin Accessory Interface	6

2.3.1 Interface Size	6

3 DP770/780/580/585 Accessory Interface	9

3.1 Interface Diagram	9

3.2 Interface Definition and Function Introduction	9

3.3 PCB Interface Layout	10

4 DP990/995/810/GP700 Accessory Interface	11

4.1 Interface Diagram	11

4.2 Interface Definition and Function Introduction	11

4.3 PCB Interface Layout	12

5 DR650/DR600/TR850 Accessory Interface	12

5.1 Interface Diagram	12

5.2 Interface Definition and Function Introduction	12

6 DM588 Accessory Interface	14

6.1 Interface Diagram	14

6.2 Interface Definition and Function Introduction	14

7 K Head Accessory Interface (for PT5200/560/4200/3300/3500(S)/3600/3800/558(S)/668/3688)	16

7.1 Interface Diagram（the same as KENWOOD）	16

8 M Head Accessory Interface（for DP405/DP415/DP480/DP485/V8/V9/S series）	17

8.1 Interface Diagram	17

9 PT7200 Series Accessory Interface（for PT7200Ex、PT7200 Plus）	18

# DP980/DP990/DP680 Accessory Interface

## Interface Diagram

Figure 1 Interface Diagram

## Interface Definition and Function Introduction

Table 1 Interface Definition

| Pin NO. | Name | Description | Features |
| --- | --- | --- | --- |
| 1 | GND | ground connection | ground connection |
| 2 | RAC_MIC_GND | Mic signal negative pole |  |
| 3 | USB_V | USB check | USB power input |
| 4 | RAC_MIC_SIG | Mic signal input | Recommended MIC sensitivity: -45±3dB ref. 1V/Pa @1kHz |
| 5 | RAC_EAR | Earphone audio |  |
| 6 | EXT_LSA | Horn output | Maximum 1.2W output, recommended load impedance 16ohm |
| 7 | EXT_LSB | Horn output | Maximum 1.2W output, recommended load impedance 16ohm |
| 8 | USB+/1_WIRE_ANCIL_DATA | USB signal input or bidirectional 1-line signal | When USB is used, USB data communication is supported. Accessory using 1 line communication protocol are supported when 1 line communication is used. |
| 9 | USB-/RAC_POWER_OUT | USB signal input or accessory power output | When USB is used, USB data communication is supported. When the accessory power supply is used: output voltage: 3V6 ± 76mV Battery voltage Vbat> 5.4V, empty load Maximum load current: 100mA |
| 10 | nRAC_PTT | Outlay PTT | Low level effective |
| 11 | RAC_ACC_ID | Accessory identification | For the identification of different types of accessory for clients |

## PCB Interface Layout

Figure 2  PCB Diagram

# DM850/TM840/DM880 Transceiver Accessory Interface

## Front Panel Microphone Interface

### Interface Diagram

Figure 3  Transceiver Front Panel Microphone Interface

## Interface Definition and Function Introduction

Table 2 Interface Definition

| Pin No. | Signal Name | Function | Signal Definition |
| --- | --- | --- | --- |
| 1 | Key_DATA | Mic Keypad Data Line input | Digital input level (2V<VIH<3.3V, High level2.0-3.3V 0V<VIL<0.8V) Low level0 - 0.8V （the same below） |
| 2 | HOOK | Mic Hook Indication | Digital input level (2V<VIH<3.3V, 0V<VIL<0.8V) |
| 3 | MIC+ | MIC+Input | Analogue Input (VIN<2.0V) |
| 4 | MIC- | MIC-Input | Analogue Input (VIN<2.0V) |
| 5 | PTT | PPT Key | Digital input level (2V<VIH<3.3V, 0V<VIL<0.8V) |
| 6 | GND | Ground | 0V |
| 7 | POWER | Mic Power Supply (7~12V) | output voltage 7-12V |
| 8 | BLC | Mic Keypad Backlight Control | Digital Output (VOH>2.8V,VOL<0.4V) |
| 9 | USB_DP | USB+ | Data input and output level USB Data (2V<VIH<3.3V,0V<VIL<0.8V) |
| 10 | USB_DM | USB- | Data input and output level (2V<VIH<3.3V, 0V<VIL<0.8V) |

### PCB Interface Layout

Figure 4 DM850/TM840/DM880 PCB Diagram

## Tail Pin Accessory Interface

### Interface Size

Figure 5 DM850/TM840/DM880 Tail Pin Interface Diagram

2.2.2Interface Definition and Function Introduction

Table 3 Tail Pin Interface Definition

| Pin No. | Signal Name | Function | Signal Definition |
| --- | --- | --- | --- |
| 1 | Ext_SWB+ | Power | +13.8V power output (Imax<1A) |
| 2 | Power Ground | Ground Connection | Ground Connection |
| 3 | USB_D+ | USB+ | USB data (2V<VIH<3.3V,0V<VIL<0.8V) |
| 4 | USB_D- | USB- | USB data (2V<VIH<3.3V,0V<VIL<0.8V) |
| 5 | USB_VBus | USB Power | +5V USB Power |
| 6 | USB_GND | USB Ground | Ground |
| 7 | Prgm_In_1(PTT) | Programmable input 1 (PTT) | digital input 2.5V<VIH<5V,0V<VIL<0.4V |
| 8 | Ext-Spk- | External horn output（SPK-） | Audio power amplifier output negative load impedance : 16Ω typical. |
| 9 | Ext-Spk+ | External horn output（SPK+） | Audio power amplifier output positive load impedance : 16Ω typical. |
| 10 | ACC_MAP_ID_2 | Accessory id line 2 | Digital input and output 2.5V<VIH<5V,0V<VIL<0.4V |
| 11 | ACC_MAP_ID_1 | Accessory id line 1 | Digital input and output 2.5V<VIH<5V,0V<VIL<0.4V |
| 12 | Prgm_IO_6 | Programmable input /output 6 | Programmable input /output 2.5V<VIH<5V,0V<VIL<0.4V 4V<VOH<5V,0V<VOL<0.4V |
| 13 | Prgm_IO_2(Monitor) | Programmable input /output 2 (monitor) | Programmable input /output 62.5V<VIH<5V,0V<VIL<0.4V 4V<VOH<5V,0V<VOL<0.4V |
| 14 | Prgm_IO_3(Chan_Act) | Programmable input /output 3 (Channel Activation) | Programmable input /output 2.5V<VIH<5V,0V<VIL<0.4V 4V<VOH<5V,0V<VOL<0.4V |
| 15 | Ground | Ground | Ground |
| 16 | Rx_Audio | Received Audio Output | Codec Audio output Wmax=15mW@32Ω |
| 17 | Audio_Ground | Audio Ground | Ground |
| 18 | Tx_Audio | Transmit Audio | External audio input(VIN<2.0V) |
| 19 | Ground | Ground | Ground |
| 20 | Prgm_IO_7 | Programmable input /output 7 | Programmable input /output 2.5V<VIH<5V,0V<VIL<0.4V 4V<VOH<5V,0V<VOL<0.4V |
| 21 | Prgm_IO_4(Emergency) | Programmable input /output 4 (Emergency) | Programmable input /output 2.5V<VIH<5V,0V<VIL<0.4V 4V<VOH<5V,0V<VOL<0.4V |
| 22 | Prgm_IO_8 | Programmable input /output 8 | Programmable input /output 2.5V<VIH<5V,0V<VIL<0.4V 4V<VOH<5V,0V<VOL<0.4V |
| 23 | Ign_Sense | Ignition | Ignition signal input 10V<VIH<16V,0V<VIL<2V |
| 24 | Prgm_Out_9(Ext_Alarm) | Programmable input /output 9 (External Alarm) | Programmable input /output 2.5V<VIH<5V,0V<VIL<0.4V 4V<VOH<5V,0V<VOL<0.4V |
| 25 | Aux_Audio_Out1 | Auxiliary audio output 1 | Wmax=15mW@32Ω |
| 26 | Aux_Audio_Out2 | Auxiliary audio output 2 | Wmax=15mW@32Ω |

# DP770/780/580/585 Accessory Interface

## Interface Diagram

Figure 6 DP770/780/DP580/DP585 Accessory Interface Diagram

## Interface Definition and Function Introduction

Table 4 DP770/780/DP580/DP585 Interface Definition

| Pin No. | Signal Name | Function |
| --- | --- | --- |
| 1 | DPTA_SEL0 | Accessory detection 0, used for the identification of different accessories |
| 2 | UART_RXD | Serial port input pin |
| 3 | NC | Void pin |
| 4 | USB+ | USB+,Signal line, used for data communication between peripheral and native machine |
| 5 | USB- | USB-,Signal line, used for data communication between peripheral and native machine |
| 6 | GND | Ground |
| 7 | EXT_SPK+ | External SPK + output |
| 8 | EXT_SPK- | External SPK- output |
| 9 | DPTA_SEL1/PTT | External PTT, accessory detection 1 multiplex signal |
| 10 | EXT_MIC+ | External MIC + signal input |
| 11 | EXT_MIC- | External MIC-Signal input |
| 12 | DPTA_SEL2 | Accessory detection 2, used for the identification of different accessories |

## PCB Interface Layout

Figure 7 DP770/780/DP580/DP585 Accessory PCB Interface Diagram

# DP990/995/810/GP700 Accessory Interface

## Interface Diagram

Figure 8 DP990/DP995 Accessory Interface

## Interface Definition and Function Introduction

Table 5 DP990/DP995 Interface Definition

| PIN No | DP990 |
| --- | --- |
|  | Name | Definition |
| 1 | SEL0 | Accessory detection, pin grounding when connecting the microphone, radio display connection icon |
| 2 | 1-Wire | Single-wire communication, refer to MOTO |
| 3 | VCC_5V | Output of 5V voltage, available with a maximum load of 300mA, and switchable |
| 4 | USB_DP/TXD | Default is USB positive, used for USB communication of programming wires; can switch to reuse UART2_TXD |
| 5 | USB_DN/RXD | Default is USB negative, used for USB communication of programming wires; can switch to reuse UART2_TXD |
| 6 | GND | Ground pin |
| 7 | eSPK+ | Horn output positive pole for the horn output of the external microphone |
| 8 | eSPK- | Horn output negative pole for the horn output of the external microphone |
| 9 | ePTT (SEL1) | Programmable IO, the default is the external PTT detection, valid grounding |
| 10 | eMIC+ | MIC input positive pole for MIC input of external microphone |
| 11 | eMIC- | MIC input negative pole for MIC input of external microphone |
| 12 | SEL2 | Programmable IO, accessory detection, grounding PIN4 and PIN5 switch to serial port |

## PCB Interface Layout

Figure 9 DP990/DP995 PCB Interface Diagram

# DR650/DR600/TR850 Accessory Interface

## Interface Diagram

Figure 10  DR650/DR600/TR850 Interface Diagram

## Interface Definition and Function Introduction

Table 6 Interface Definition

| Pin No. | Signal Name | Function | Signal Definition |
| --- | --- | --- | --- |
| 1 | Ext_SWB+ | Power Supply | +13V Output |
| 2 | Power Ground | Ground | 0V |
| 3 | USB_D+ | USB+（alternate） |  |
| 4 | USB_D- | USB-（alternate） |  |
| 5 | USB_VBus | USB Power（alternate） |  |
| 6 | USB_GND | USB Ground | 0V |
| 7 | Prgm_In_1(PTT) | External PTT Signal input, High level active .when connected with Pin20, enter transmission mode | Digital Input (2.5V<VIH<3.3V, 0V<VIL<0.4V) |
| 8 | Ext-Spk- | External SPK- output | 8 Ω /16Ω, 0.8W Max |
| 9 | Ext-Spk+ | External SPK+ output | 8 Ω /16Ω, 0.8W Max |
| 10 | ACC_MAP_ID_2 | Accessory ID input Line 2 Control signal, when connected with Pin20, mode of analog RX performance testing | Digital input level (2.5V<VIH<5V, 0V<VIL<0.4V) |
| 11 | ACC_MAP_ID_1 | Accessory ID input Line 1 Control signal, when connected with Pin20, mode of analog RX performance testing | Digital input level (2.5V<VIH<5V,0V<VIL<0.4V) |
| 12 | Squelch Prgm_IO_6 | Digital Input. High level will enable opening squelch when connected with Pin20. | Input output level (2.5V<VIH<5V, 0V<VIL<0.4V) |
| 13 | RXD | Output. Receive signal from repeater to PC | RS232 Level: -3V ~ -15V +3V ~ +15V |
| 14 | TXD | Input. Transmit signal from PC to repeater | RS232 Level: -3V ~ -15V +3V ~ +15V |
| 15 | Ground | Ground | - |
| 16 | Rx_Audio | Void | - |
| 17 | Audio_Ground | Audio Ground | - |
| 18 | Tx_Audio | TX audio External audio input | External audio input, the voltage is less than 0.5 volts (VIN<0.5V) |
| 19 | Ground | Ground | 0V |
| 20 | Prgm_IO_7 | Output high level, used with Pin7 (PTT function), Pin10 (analog Rx function) and Pin11 (IP address reset function) and pin23(open squelch) | Input output level (2.5V<VIH<3.3V, 0V<VIL<0.4V) |
| 21 | Program_IO_4 (Emergency) | Not Available | - |
| 22 | Prgm_IO_8 | Not Available | - |
| 23 | Program_IN_5 | Digital Input High level active Opening squelch when connected with Pin20 | Digital Input: (2.5V<VIH<5V,0V<VIL<0.4V) |
| 24 | Prgm_Out_9(Ext_Alarm) | Reserved | - |
| 25 | Aux_Audio_Out1 | Not Available | - |
| 26 | Aux_Audio_Out2 | Not Available | - |

# DM588 Accessory Interface

## Interface Diagram

Figure 11  DM588 Interface Diagram

## Interface Definition and Function Introduction

Table 7 Interface Definition

| Pin No. | Signal Name | Function | Signal Definition |
| --- | --- | --- | --- |
| 1 | USB_DM | USB+ |  |
| 2 | MIC+ | MIC+ |  |
| 3 | MIC- | MIC- |  |
| 4 | USB_DP | USB- |  |
| 5 | HOCK | HOCK/void pin |  |
| 6 | CM | CM keyboard/void pin |  |
| 7 | PTT | PPT Key |  |
| 8 | BL_MIC | Mic Keypad Backlight Control |  |
| 9 | POWER | Power |  |
| 10 | GND | Ground |  |

# K Head Accessory Interface (for PT5200/560/4200/3300/3500(S)/3600/3800/558(S)/668/3688)

## Interface Diagram（the same as KENWOOD）

(Purplish red-MIC +, Copper yellow -PTT Control, Green-Horn, Blue-Ground Com）

# M Head Accessory Interface（for DP405/DP415/DP480/DP485/V8/V9/S series）

## Interface Diagram

（Copper yellow -PTT Control、Purplish red-MIC +、Green-Horn+、Dark blue-Ground）

# PT7200 Series Accessory Interface（for PT7200Ex、PT7200 Plus）

| Pin No. | Signal Name | Function |
| --- | --- | --- |
| 1 | SPK+ | power amplifier audio output+ |
| 2 | EXT_MIC | Ext MIC+ input |
| 3 | OPT_S1 | Accessory identification, low level is effective. |
| 4 | RXD | RXD data wire |
| 5 | XC | XC |
| 6 | XC | XC |
| 7 | SPK- | power amplifier audio output- |
| 8 | EXT_VCC | 7.4V power supply |
| 9 | EXT_PTT | EXT PTT input |
| 10 | GND | Ground |
| 11 | TXD | TXD data wire |
| 12 | XC |  |
| 13 | NC |  |